## Slide 1: Antenna Course 19-May-2015 Lecture 11
Dr. Andrés Alayón Glazunov

## Slide 2: Learning goals
Know the operational principle and advantages of array antennas
Explain the analysis of linear phased array
  Array factor as element-by-element sum
  Array factor as grating-lobe sum.
Describe the difference between isolated and embedded element patterns
Calculate Directivity, positions of grating lobes

## Slide 3: Lecture 11 Linear Array Antennas
Introduction to Array Antennas
Isolated element pattern vs. embedded element pattern
Linear array
  Array factor as element-by-element sum
  Array factor as infinite grating lobe sum
Example: Long linear array

## Slide 4: Many Applications
Communications
  Satellite, cellular, microwave links
Radio astronomy
Radar
  Automotive, weather, seismology, defense
Biomedicine

## Slide 5: The need for large antenna aperture area
So far we have mainly considered single (-element) antennas and their characteristics.
Usually these antennas have wide beamwidth and thus low directivity
As we have seen, there are many applications where high directivity is needed
Antennas must then become electrically large, i.e., become larger than a wavelength 
Why?

## Slide 6: Key design rules of antennas (A  Dmax)
For an antenna with the aperture area A,
the maximum directivity (gain?):
Big aperture (uniform excitation)
Small aperture

## Slide 7: How to create an antenna with a big aperture?
10λ
5λ×5λ
5λ
1. Big dipole?
3. Big horn?
4. Reflector antenna?
2. Big patch?

## Slide 8: But
Horn and reflector have big volumes.
Any other way?
What if we use several antennas in some ”intelligent” way?
Can we gain anything from it?
How to analyze this new antenna system?

## Slide 9: What is an array?
Array is a collection of antennas (known as elements) which are integrated within one module, together with electronic circuits.
The signals are combined in the optimal way (the procedure named ‘beam-forming’) to achieve the enhanced performance as compared to that of a single antenna.
Power distribution network
(or beam-forming network).
4 patch antenna elements

## Slide 10: Operational principle
https://www.youtube.com/watch?v=LNXVod90mVw
https://www.youtube.com/watch?v=gZkFVco4kL4
Far-field function
Single aperture
antenna

## Slide 11: Operational principle
Far-field function
Single aperture
antenna
Array of two identical
aperture antennas
How does the total array far-field function look like?

## Slide 12: How does the total array far-field function look like?
A. The same as the far-field function the
single aperture with 3dB higher directivity
B. The same as the far-field function of the 2x
bigger aperture with the uniform excitation
C. The same as the far-field function of the 2x
bigger aperture with non-uniform excitation
D. Other?

## Slide 13: Array beam is formed through interferance of complex far-field functions of array elements
What should be changed in the array to form this far-field function?

## Slide 14
How to control the shape of the array beam?
Inter-element separation distance
Excitations of elements
Pencil beam
Multiple beams
Shaped beam
Number of elements

## Slide 15: Array and element types
  Spatial arrangement
  linear, planar, conformal (spherical, cylindrical or any other)
  Full scan, i.e., 60, or limited scan arrays
  Antenna element types can be arbitrary
  Dipole elements, waveguide slot elements
  Microstrip patch elements, helix/spiral elements
  Open waveguides or horns
  Reflector antennas (interferometers)

## Slide 16: Assumptions in this course
Uniform element spacing will be considered
non-uniform element spacing

## Slide 17: Assumptions in this course
Uniform element spacing
Single-mode antenna elements
  J or M distribution on antenna element can be described by a single-mode (single function).
Single-mode antennas
  The shape of the J or M distribution on antenna element is independent of how element excited.
Multi-mode antennas (complex elements, strong mutual coupling and edge truncation effects)

## Slide 18: Arrays compared to horns and reflectors
Advantages:
  can be made flat or conformal
  phase steering (beam direction change)
  full pattern control (beam shaping)
  multiple beams (flexibility)
  signal processing capability (beam shape optimization)
  digital beam-forming (real-time re-configuration of beam-forming scenario)
The Phased Array Radar pyramid
at RAF Fylingdales (Yorkshire CND)
Space Surveillance Network
Arecibo Radio Telescope,
305 meters in diameter
Disadvantages:
   more expensive (not always)
   more complicated

## Slide 19: Dipole array with the individual element control for each element (more flexibility, but expensive)
Different realizations of array feeding methods
Linear microstrip patch arrays with the reduced number of controls
(easy to integrate with electronics  compact, lower costs)
series-fed arrays
(one feed only)
parallel-fed arrays

## Slide 20: Example of a series-fed array Slot phased array in Lab 2

## Slide 21: Different realizations of array beam-forming networks

## Slide 22: Array antennas are a part of the MIMO technology
MIMO (Multiple Input Multi Output)
Array antennas are used in
  Beam forming/beam steering
  Spatial division multiple access
  Cell-shaping
  As well as
  spatial multiplexing
  diversity
Not MIMO!

## Slide 23: Lecture 11 Linear Array Antennas
Introduction to Array Antennas
Isolated element pattern vs. embedded element pattern
Linear array
  Array factor as element-by-element sum
  Array factor as infinite grating lobe sum
Example: Long linear array

## Slide 24
Isolated element pattern
No other elements around
The structure remains, such as the ground plane.
Embedded element pattern
All elements and structure exist.
All other elements terminated with load
Only one element excited.
Load
Load
Load

## Slide 25: Illustration for a point source array
Embedded element pattern
excited element
terminated element
Will this element radiate too?
What is the shape of the far-field function of this element?

## Slide 26: Illustration for the linear array of 2 point sources
Embedded element pattern
Interference region
(occurring due to mutual coupling effects)

## Slide 27: Lecture 11 Linear Array Antennas
Introduction to Array Antennas
Isolated element pattern vs. embedded element pattern
Linear array
  Array factor as element-by-element sum
  Array factor as infinite grating lobe sum
Example: Long linear array

## Slide 28: Now let us analyze linear phased array to find its far-field function

## Slide 29: Linear Array of Equispaced Elements
Elements are located with their phase reference points at
N equispaced and identical antenna elements.
Length of array: L = Nda
rc is the geometrical center of the array
is a unit vector along the direction of the array axis
da is the element spacing

## Slide 30: Radiation field function of an array element
For element number n the radiation field at the observation point r:
 the far-field function, defined
at its reference point
Far-field function, defined at the origin of the coordinate system of the whole array

## Slide 31: Radiation field function of the array antenna
Radiation field function of the whole array:

## Slide 32: Radiation field function of the array antenna
Radiation field function of the whole array:
the amplitude of the current (voltage) excitation
the phase of the current (voltage) excitation
(SUPERPOSITION)
sum of the array element far-field functions, weighted with the complex-valued excitation coefficients

## Slide 33: Radiation field function of the array antenna
Array Factor:
AF is expressed as an element-by-element sum
 the complex far-field function at its reference point
Radiation field function of the array:

## Slide 34: Example: Array Factor for uniform amplitude and linear phase
Amplitude excitation is the same for all elements (‘uniform’):
A1
AN
An
A2
0
-ΔΦ
-2ΔΦ
-3ΔΦ
n=1
n=2
n=3
n=4
n
da
da
da
N
a1
a2
a3
a4
an
aN
Phase excitation progresses linearly along the array (‘linear phase’):
N
1
+
F
n
F
c
n
2
-
-
-
-
-
-
-
-
-
-
-
-
-
–
è
ø
æ
ö
–
=
(-DF)
[rad]
 phase difference between
neighboring elements
DF
kF = -DF /da
 propagation constant for the phase progression
along the array

## Slide 35: Array factor for uniform amplitude and linear phase
Array factor becomes:
[rad]
Projection of the observation direction along the direction of the array
=

## Slide 36: Array factor for uniform amplitude and linear phase
The array factor becomes by using sum of geometrical series:

## Slide 37: Direction of maximum radiation
direction in which the fields radiated by the array elements are added constructively (in-phase)
= 0
a0
cos(a0)= -ΔΦ /(kda)
For a linear array with da and fixed ΔΦ:
main lobe direction
ka = kΦ kcos(a0)= -ΔΦ /da

## Slide 38: Linear array: Main lobe direction
When the phase progression changes
Steered main lobe
defines main lobe or main beam cone around the axis.

## Slide 39: Linear array: Steered main lobe direction
Beam steering by changing :
http://www.youtube.com/watch?v=VBFsisCjpBk

## Slide 40: Illustration of the AF for linear array of given length L for different number of elements N
(cos() is a variable for a given L/ and N)

## Slide 41: Now let us use another method to find far-field function of Linear array
Analysis of the AF expressed through the element-by-element sum becomes
time-consuming for large arrays

## Slide 42: Lecture 11 Linear Array Antennas
Introduction to Array Antennas
Isolated element pattern vs. embedded element pattern
Linear array
  Array factor as element-by-element sum
  Array factor as infinite grating lobe sum
Example: Long linear array

## Slide 43: Definition of excitation function
Amplitude excitation function: A(a) – (‘non-uniform’)
Phase excitation function:
(‘linear phase’)

## Slide 44: Array Factor
ka=kcosα
kΦ=-ΔΦ /da
A(a) is zero for a < -L/2 and a > L/2, which corresponds to
n < 1 and n > N

## Slide 45
Periodic function with period da
Poisson summation formula

## Slide 47: Array factor as infinite grating lobe sum
This result is related to the results obtained for apertures and wires …
Fourier transform of the amplitude excitation distribution A(a):

## Slide 48: Array factor as infinite grating lobe sum
Fourier transform describes the shape
of the AF around a direction corresponding to
The infinite sum converges fast for large arrays (often only the dominant p=0 and p=1 need to be included)
p=..-2,-1,1,2..

## Slide 49: Graphical representation of array factor and element factor
=
The AF is a function of

## Slide 50: Graphical representation of total array pattern
=0
A(a) = 1 and ΔΦ = 0
ka/k
=0

## Slide 51
=
When varies
=0
When varies, the AF is translated along the axis

## Slide 52
A(a) = 1 and ΔΦ = k da/2
Graphical Representation of total pattern

## Slide 53: Linear array: Grating lobes
Grating lobes at
p=..-2,-1,1,2..
Requirement for non-radiating grating lobes

## Slide 54: Example: Uniform excitation distribution
If
, and ΔΦ=0, we get
For tapered excitations
will get lower sidelobes

## Slide 55: Linear array: Some basic Principles
The neccesary condition for avoiding grating lobes is da<λ.
The sufficient condition for avoiding grating lobes is da<λ/2.
The element spacing da should be
to avoid grating lobes for certain maximum beam direction α0 .

## Slide 56: Some Notes about Array Factor
Element-by-element
General, always valid.
  Any element spacing;
  Any type of excitations;
  Any size of the array;
  Valid also for sparse arrays;
Do not provide the insight of the grating lobes
For large array, computation time for AF is long.
Sum of grating lobes
Not generally valid
  Equal spacing;
  linear phase excitation;
  Large array
Give you the insight of the grating lobes
  When you have a grating lobes;
Easy to have analytical formulas for directivity, etc.

## Slide 57: Lecture 11 Linear Array Antennas
Introduction to Array Antennas
Isolated element pattern vs. embedded element pattern
Linear array
  Array factor as element-by-element sum
  Array factor as infinite grating lobe sum
Example: Long linear array

## Slide 58: Directivity of a long linear array
Far-field function:
The power integral:
For simplifying the power intergral we
locate the linear array along the z axis.
Therefore, AF has no φ variation
x
y
z

## Slide 59: Directivity of a long linear array
Finally

## Slide 60: Directivity of a long linear array
For uniform distribution , Dθ =2L/λ
Directivity in the longitudinal -plane
Due to array distribution

## Slide 61: Directivity of a long linear array
Directivity on the main lobe cone
Due to element pattern
If G has no φ variation and no cross polar, Dφ= 1=0dB
Remember the definition of the coordinate system.

## Slide 62: Directivity of a long linear array
Grating lobe efficiency
If we have
p for all grating lobes in the visible region

## Slide 63: How to control the shape of the array beam?
There are five basic methods to control the overall antenna pattern:
the geometrical configuration of the overall array (linear, planar, conformal, etc.),
the relative placement of the elements,
the excitation amplitude of the individual elements,
the excitation phase of each element,
the individual pattern of each element

## Slide 64: Learning goals
Know the operational principle and advantages of array antennas
Explain the analysis of linear phased array
  Array factor as element-by-element sum
  Array factor as grating-lobe sum.
Describe the difference between isolated and embedded element patterns
Calculate Directivity, positions of grating lobes