## Slide 1: Lecture 14 Materials for antenna design & Fundamental limitation of antennas By Ashraf Uz Zaman zaman@chalmers.se

## Slide 2: Content
Boundary conditions, a short repetition
Materials for antenna design
  PEC, PMC, PEC/PMC strip grids (soft and hard surfaces)
  Bandgap surfaces
Fundamental limitation of antennas
  Directivity limitations
  Efficiency limitations
  Bandwidth limitations

## Slide 3: Learning Goals
Describe the most common materials used in numerical analysis as well as in practical antenna design.
Explain the directivity limitations of large and small antennas.
Describe the efficiency and bandwidth limitations of single-port antennas and multi-port array antennas

## Slide 4: Boundary conditions
General (surface currents cause discontinuous tangential E- and H-fields):
On dielectric material (continuous tangential E- and H-field):
On PEC
On PMC (does not exist naturally):
Surface current density

## Slide 5: Soft and hard surfaces originate from acoustics and diffraction theory p is acoustic pressure
Surface | Boundary condition | Wave propagating at surface
Soft |  | No
Hard |  | Yes

## Slide 6: PEC: Wave propagation along surface
VER propagation GOes with at surface.
HOR polarization STOPs with at surface
EHOR
J
EVER
J

## Slide 7: Fields around PEC, 2D case Soft and hard boundary conditions
Soft boundary condition Hard boundary condition
BC on all materials affects vertical and horizontal polarizations differently.

## Slide 8: What are metamaterials?
Metamaterials are artificial materials, with abnormal characteristics
  Appears unphysical, but may not be
  Often narrow band, but not always
Metamaterials are realized by periodic elements in a 1D, 2D or 3D grid.
Artificial dielectrics have been known for several decades
Frequency Selective Surfaces as well (plane wave filters)

## Slide 9: Explanations of Abbreviations
GO surfaces: Enhances propagation of waves along surface
STOP surface: Stops propagation of waves along surface
PEC : Perfect Electric Conductor
PMC : Perfect Magnetic Conductor
AMC : Artificial Magnetic Conductor
PBG : Photonic Bandgap Material
EBG : Electromagnetic Bandgap Material

## Slide 10: Soft and hard surfaces originate from acoustics and diffraction theory p is acoustic pressure
Surface | Boundary condition | Wave propagating at surface
Soft |  | No
Hard |  | Yes

## Slide 11: Soft and hard surfaces in electromagnetics
Type of surface | Boundary condition | Wave propagation at surface
Smooth conductor |  | STOP for HOR pol. GO for VER pol.
Wave direction
VERtical polarization
HORizontal pol.
Soft surface |  | STOP for HOR pol. STOP for VER pol.
Hard surface |  | GO for HOR pol. GO for VER pol.

## Slide 12: PEC/PMC strip model of ideal soft and hard surfaces
Ideal soft surface = STOP surface
Ideal hard surface = GO surface
Current fences
Current lanes

## Slide 13: PEC/PMC strip surface can be either soft or hard, depending on plane of incidence

## Slide 14: Definition of Soft and Hard Surface
is the longitudinal direction and is the direction of the Poynting vector and power flux. (Green)
is the transverse direction and is also orthogonal to the longitudinal direction.(Red)
Surface impedences are:

## Slide 15: Realization of soft and hard surfaces with corrugations Soft STOP surface Hard GO surface
Transverse air-filled corrugations
(current fences)
Longitudinal dielectric-filled corrugations
(current lanes)

## Slide 16: Soft surface: Principle of operation for transverse corrugations (current fences)
EVER sees AMC (transformation from short-circuit to open-circuit in grooves)
EHOR sees PEC.
No penetration into grooves.

## Slide 17: Soft surface: Bandwidth is limited by surface waves
Ideally large 2:1 bandwidth
d
p
w

## Slide 18: Hard surface We MUST have dielectric filling to get field transformation
EHOR
d
Bandwidth small due to dispersive surface wave near cut-off.

## Slide 19
EBG surfaces are characterized from the dispersion diagram for the guided wave
G
X
M
Y
G
Frequency (GHz)
0
4
8
12
16
18
Band-gap
Y
G
X
M
Sievenpiper 1999:
Mushroom surface
Forbidden frequency bands
Electromagnetic bandgap
(EBG) surface
Notes: EBG surfaces are, in most studies, planar with 2-
D periodic structure, along which the surface
wave propagation is forbidden in a certain
frequency band, i.e., there is a bandgap in the
dispersion diagram of the surface wave. The
quality of the EBG surface is often measured in
terms of the size of the bandgap.
Original EBG structures have the form of metal patches on a planar grounded
dielectric slab, with metalized via holes connecting the centre of the patches and the
ground plane.

## Slide 20: Comparison between different canonical surfaces with respect to waves propagating along the surface

## Slide 21: Applications
Soft surfaces:
Shielding for EMC
  reduce transmission through gaps
  polarization-independent shields
  reduce coupling along surfaces and over corners
Feeds for reflector antennas
  soft horns for low sidelobes and cross-polarization and symmetric beam
Sidelobe control in antennas
Hard surfaces:
Cloaking, reduce sidelobes due to structure
  masts, struts
  spaceframe radomes
Reduce radar cross-section
Array antennas, quasi-TEM waveguides
  compact hard horn elements
  grid amplifiers
  TEM feed lines for slot arrays and more
  waveguide simulators for dual polarization and broadside radiation

## Slide 22: Soft and hard surfaces are useful! Hat feed in ring-focus paraboloid, Kildal 1986
Low sidelobes
Good efficiency
Due to a soft surface

## Slide 23
Cloaking with hard surfaces
Without
cloak
With
cloak
Support struts cause sidelobes due to blockage.
Kildal et al 1996: Struts can be made invisible by HARD surface cloak

## Slide 24
Problems of conventional waveguide at high frequency
At high frequency, traditional milling or machining techniques for waveguide components are very complicated and costly.
Very good electrical contact and alignment is necessary between the metal split blocks.
High-quality surface finishing over the whole metal contact area is required for good mechanical assembly.
Mechanical assembling presents major bottleneck.

## Slide 25
Gap waveguide

## Slide 26
Gap waveguide (Different Versions)

## Slide 27
Gap waveguide (Different Versions)

## Slide 28
Ridge Gap waveguide with bed of nails
10 GHz
11 GHz
12 GHz
13 GHz
14 GHz
15 GHz
16 GHz
17 GHz
18 GHz
19 GHz
20 GHz
9 GHz
22 GHz
21 GHz

## Slide 29
Various Gap waveguide components

## Slide 30
Gap waveguide Packaging

## Slide 31
Gap waveguide Packaging
Quite smooth S21 when packaged
with pin lid.

## Slide 32: Summary
Surface name | Boundary condition | Function | Best realization | Application
PEC | Simple Etan=0 | Symmetry plane in EM simulations. Represents well good conductor | Smooth metal | Everywhere
PMC (AMC) | Simple Htan=0 | Symmetry plane in EM simulations. Together with PEC to create parallel-plate cut-off | Bed of nails, pin surface | as ground plane of dipoles, in gap waveguides
PEC/PMC strip grids | Simple Ex=0. Hx=0. | Soft case: Stops waves in transverse direction. Hard case: Enhances waves in longitudinal direction. | Corrugations and similar | Horn antennas,
EBG | No simple BC exists | Stops waves in all directions along it. | 2D periodic planar | Reduce sidelobes and mutual coupling
FSS | Transparent in band, reflective outside | Frequency filter for waves in free space | 2D periodic planar | Multiband antennas

## Slide 33: Content
Boundary conditions, a short repetition
Materials for antenna design
  PEC, PMC, PEC/PMC strip grids (soft and hard surfaces)
  Bandgap surfaces
Fundamental limitation of antennas
  Directivity limitations
  Efficiency limitations
  Bandwidth limitations

## Slide 34: Literature
The two papers:
Nyberg, Kildal, Carlsson, “Effects of intrinsic radiation Q on mismatch factor of three types of small antennas: Single-resonance, gradual-transition and cascaded resonance types”, published in IET 2010
Per-Simon Kildal, “Fundamental directivity and efficiency limitations of single- and multi-port antennas”, EuCAP 2007 paper

## Slide 35: Directivity limitations: Large antennas
Well known formula from aperture theory
Maximum available directivity Dmax is:
Diameter D
A is aperture area

## Slide 36: Incremental sources and small antennas
Name | Spherical mode excited | Example | Realization | Direc-tivity
Electric dipole | First TM |  | Straight wire | 1.8 dBi
Magnetic dipole | First TE |  | Wire loop | 1.8 dBi
Huygen’s source | First TE&TM |  | Optimum combination | 4.8 dBi (i.e. 3)

## Slide 37: Argumentation for maximum available directivity of small antenna
The basic incremental sources are electric and magnetic dipoles
These excite the fundamental TM- and TE-modes.
No other modes can exist for small enough source due to cut-off of spherical modes)
The Huygen´s source is the combination of electric and magnetic current sources that gives the highest directivity, 4.8 dBi.
Thus, there cannot exist small antennas with larger directivity than this, i.e. 4.8 dBi.

## Slide 38: Heuristic combination of directivity limitation formulas
The below formulas are valid for any diameter D of smallest enclosing sphere
D
D

## Slide 39: Fundamental limitations & practical antennas

## Slide 40: Directivity limitations: Planar arrays
Same heuristic formula applies by using aperture theory for arrays
‘A’ is aperture area including whole unit cell along boundaries,
i.e. the green area in the drawing.
dy
dx
Nxdx
Nydy
correct area
Wrong area

## Slide 41: Content
Boundary conditions, a short repetition
Materials for antenna design
  PEC, PMC, PEC/PMC strip grids (soft and hard surfaces)
  Bandgap surfaces
Fundamental limitation of antennas
  Directivity limitations
  Efficiency limitations
  Bandwidth limitations

## Slide 42: Radiation efficiency can be measured in reverberation chamber

## Slide 43: Total radiation efficiency: contributing factors
Single-port antennas
  Losses due to the materials the antenna is made of.
  Losses due to materials of near-in objects (like human head when dealing with phone antennas)
  Mismatch factor (limitation described by intrinsic radiation Q)
Multi-port antennas
  In MIMO arrays we have defined an embedded element efficiency
  Generally, we can define a coupling efficiency which replaces mismatch efficiency for general excitations

## Slide 44: Decoupling efficiency
Is due to losses in neighboring ports when one port is excited

## Slide 45: Content
Boundary conditions, a short repetition
Materials for antenna design
  PEC, PMC, PEC/PMC strip grids (soft and hard surfaces)
  Bandgap surfaces
Fundamental limitation of antennas
  Directivity limitations
  Efficiency limitations
  Bandwidth limitations

## Slide 46: Quality Factor of Resonator
fo
Δf3dB
By measurement:
Can be estimated from theoretical results at one frequency f0 only:
Q is linked with losses

## Slide 47: Fundamental limitations of small antennas
Pre-PC era: Radiation Q
  Chu, 1948: Intrinsic Q limitation
  Small antennas were resonators
  Bandwidth could be determined by evaluation at center frequency using Q
PC era: What is Q useful for?
2a

## Slide 48: Single-port antennas: Intrinsic radiation Q determines
Single-resonance-type antenna
  Relative bandwidth
Wideband gradual-transition-type antenna
  Lower cut-off frequency
Wideband multiple-resonances-type
  Number of cascaded resonant elements needed
Losses are larger for resonant antennas than for non-resonant,
but NO FUNDAMENTAL LIMITATION on losses are known.

## Slide 49
Intrinsic radiation Q:
Basic TE or TM mode:
(Chu, Collin, McLean, ...)
Matching
Antenna
a
Equivalent circuit of resonant antenna
Size vs. Q
TE
TM
Any combination of basic TE and TM modes:
(Harrington, Kwon)
Q is linked with size

## Slide 50
Single-resonance type of antenna
2. Wideband gradual-transition-type small antennas
3. Multiple resonance-type small antennas
Different types of Antennas
2a
2a
2a

## Slide 51
Matching
Antenna
Single resonance: Q
1)
2)
3)
2a
Qintrinsic represent a fundamental limitation on the
bandwidth-efficiency product.
Q is linked with matching.

## Slide 52
The emismatch= -3 dB bandwidth plotted vs antenna size.
Single resonance: Bandwidth
Qintrinsic represent a fundamental limitation on the
bandwidth-efficiency product.
Appr. formula
2a

## Slide 53
No matching
Antenna
No matching network
No resonances
What is Q then?
Gradual transition: Q
2a
Use fundamental limitations on Q to get fcutoff
Mismatch factor:

## Slide 54
Gradual transition: Q determines gradual cut-off
Q represents the cut-off frequency
ka = 1 relates the gradual cut-off for the first spherical modes to the cut-off frequency for small antennas
Mismatch factor (dB)

## Slide 55
The bandwidth can be increased by using multiple resonances.
Examples:
The log-periodic dipole array
The 11 –antenna. The BW is increased by adding elements, the volume is constant!
Multiple resonance
Higher Q = steeper slope of RL

## Slide 56: Example of S11 and mismatch factor for theoretical multiple-resonance-type antenna with 6 cascaded resonances (simplified model)

## Slide 57
Single resonance-type
  Qintrinsic is a fundamental limitation on the bandwidth-efficiency product.
Gradual transition-type
  Q defines the gradual cut-off frequency.
Cascaded resonance-type
  The number of resonances needed depends on Q, effects the scaling factor.
  Q determines the slope of RL at end frequencies.
Conclusions