## Slide 1: 8. Horn Antennas Lecturer: Per-Simon Kildal
&
corrugated pyramidal and conical horns

## Slide 2: Learning goals
Describe far field functions in E- and H-plane of different horns with rectangular aperture (and why they have certain shape):
  E-plane sectorial, H-plane sectorial, pyramidal, corrugated E-plane walls
Describe far field function in E-plane, H-plane and 45 deg plane of different horns with circular aperture (and why they have certain shape):
  Smooth wall, corrugated wall.
Describe the Gaussian beam model for corrugated conical horns
After exercise: Apply Gaussian beam model to design corrugated conical horn

## Slide 3: Literature
Chapter 8 in compendium. Horn antennas.
Mandatory literature:
  The whole chapter except the supplementary Sections 8.1.1, 8.1.2, 8.1.3, 8.1.5, 8.1.6, 8.2, 8.3, 8.4

## Slide 4: Calculation Methods
Different analytical and numerical methods:
  Approximating the aperture field by using the basic propagating mode inside the horn
  mode matching
  moment method
  finite element method (FEM)
  finite difference time domain technique (FDTD)

## Slide 5: Cylindrical waveguide plane aperture approach
Aperture field given by excited single mode propagating in waveguide
Use PEC or free space equivalence
Open waveguides in infinite ground plane.
Only accurate
with ground plane.

## Slide 6: Flared cylindrical waveguide approach
Use cylindrical waveguide mode over curved
aperture.
Paraxial approximation
Huygen’s equivalent
Advantages:
Simple analytic form & Universal rad. patterns

## Slide 7: Flared cylindrical waveguide approach Sector horn antenna
Cylindrical wave modes propagating in radial direction
free space equivalent over cylindrical aperture surface
Paraxial approximation and Huygen’s equivalent
Advantages:
  Simple analytic form
  Universal rad. patterns

## Slide 8: Conical and spherical sector waveguide approach
Spherical wave modes propagating in radial direction
free space equivalent over spherical aperture surface.

## Slide 9: Mode matching approach

## Slide 10: Moment method approach cont.

## Slide 11: Example: Pyramidal horn
E-plane pattern is equal to that ot the E-plane sector horn.
H-plane pattern is equal to that of the H-plane sector horn.

## Slide 12: We will use this classical approach: Flared cylindrical waveguide approach
Use cylindrical waveguide mode over curved
aperture.
Paraxial approximation
Huygen’s equivalent
Advantages:
Simple analytic form & Universal rad. patterns

## Slide 13: Small E-plane sectoral horn: Radiation pattern
a=0.5l, b=2.75l, L=6l

## Slide 14: Small H-plane sector horn: Radiation pattern
a=5.5l, b=0.25l, L=6l

## Slide 15: Example: Pyramidal horn
E-plane pattern is equal to that of the E-plane sector horn.
H-plane pattern is equal to that of the H-plane sector horn.
Important parameter is this
maximum phase error in aperture

## Slide 16: Universal E-plane pattern: for both E-plane sector horn and pyramidal horn

## Slide 17: Universal H-plane radiation pattern: for both H-plane sector horn and pyramidal horn

## Slide 18: Pyramidal horn: Universal contour pattern (when max phase variation over aperture is 90°)

## Slide 19: Smooth conical horn (BOR1)
BOR1 excitation
Basic TE11 mode in a circular cylindrical waveguide
for
where

## Slide 20: Smooth conical horn: Far field function
Radiation field function:
with

## Slide 21: Smooth conical horn: Universal radiation pattern in 45° plane
E- and H-planes:

## Slide 22: Smooth conical horn: Co- and crosspolar contour plots for max phase error = 90°
Aperture fields:
Far fields:

## Slide 23: Corrugated horns and surface Corrugations are used to improve E-plane performance and 45 deg cross polarization

## Slide 24: Universal E-plane radiation patterns for pyramidal horns with and without corrugations
Without corrugations
“uggly” radiation patterns
With corrugations
Nice radiation patterns

## Slide 25: PEC/PMC strip model of ideal soft and hard surfaces
Ideal soft surface = STOP surface
Ideal hard surface = GO surface
Current fences
Current lanes

## Slide 26: Corrugated pyramidal horn: Aperture field
Construct aperture field by using
at the smooth PEC walls,
on the corrugated soft wall.
Field solution inside rectangular corr. waveguide:
When all four walls are corrugated, the field solution is
approximately the same for any polarization.
Same results in E- and H-plane (if a=b)
Both equal to universal H-plane pattern of H-plane sector horn.
and
Aperture field:

## Slide 27: Corrugated surface: Bandwidth and surface waves
The usable bandwidth is within the range
i.e.
In practice usable relative bandwidth up to 1.8.
Best soft E-plane performance is when
or
Surface waves may exist when:

## Slide 28: Examples of corrugated conical horns, one with lens

## Slide 29: Corrugated horns were used in earth stations like this one

## Slide 30
Circular waveguide with PEC wall:
With soft wall:
No x-pol, field zero at wall in all planes, known from corrugated horns

## Slide 31: Corrugated soft conical horn: Aperture field
Corrugated circular cylindrical waveguide (hybrid mode)
where
is the value of x for the first null of
Approximate aperture field

## Slide 32: Corrugated soft conical horn: Radiation field function
Far field function:

## Slide 33: Universal radiation patterns in 45° plane of circular horns without (uggly) and with (nice) corrugations
without corrugations with corrugations

## Slide 34: Smooth conical horn: Co- and crosspolar contour plots for max phase error = 90°
Aperture fields:
Far fields:

## Slide 35: Corrugated conical horn: Co- and crosspolar contour plots for max phase error = 90°
Aperture fields:
Far fields:

## Slide 36: Modelling corrugated horn antennas by using Gaussian beams
Aperture distribution for linearly y-polarization:
Approximate this as Gaussian aperture distribution:

## Slide 37: Design curve for corrugated horn: Directivity of Gaussian beam with given taper at given beam angle
(for determining desired directivity of corrugated horn)

## Slide 38: Design curve for corrugated horn: Directivity as a function of horn size and flare angle
Determines horn size if desired directivity is known

## Slide 39: Design curve for corrugated horn: Location of phase center
Zpc=0 corresponds to aperture plane.
Aperture-controlled above dashed line.
Flare-angle controlled below red dashed line.
D
a

## Slide 40
Broadband SOFT corrugated primary feed
(Ying,
A. Kishk and
P-S. Kildal, 1995)

## Slide 41: Learning goals
Describe far field functions in E- and H-plane of different horns with rectangular aperture (and why they have certain shape):
  E-plane sectorial, H-plane sectorial, pyramidal, corrugated E-plane walls
Describe far field function in E-plane, H-plane and 45 deg plane of different horns with circular aperture (and why they have certain shape):
  Smooth wall, corrugated wall.
Describe the Gaussian beam model for corrugated conical horns
After exercise: Apply Gaussian beam model to design corrugated conical horn