## Slide 1: Lecture 8 Small Antennas – Part 1
What is a small antenna?
Monopole and dipole antennas
Loop antenna
Helical antennas
Slot antennas
Yagi antennas
Log-periodic wideband antennas
Jian Yang
jian.yang@chalmers.se
Room 7312

## Slide 2: Learning outcomes of the Lecture
Describe the definition of small antennas.
Describe at least five types of small antennas.
Describe characteristics of the radiation function of these small antennas, such as the directivity and radiation resistance.
Explain the analysis models for these small antennas.

## Slide 3: Lecture 8 Small Antennas – Part 1
Dipole
- Assume current
distribution
- Calculate directivity
and radiation impedance
- …
Monopole
Loop antenna
Helical antenna
Slot antenna
Yagi antenna
Log-periodic array
Basis
Using different methods to extend the results to different antennas

## Slide 4: Lecture 8 Small Antennas – Part 1
What is a small antenna?
Monopole and dipole antennas
Loop antenna
Helical antennas
Slot antennas
Yagi antennas
Log-periodic wideband antennas

## Slide 5: What is a small antenna?
Radiostationen i Grimeton, Long wave antenna, 17.2 kHz
Mobile phone antenna
(not this years model)
Height 127 m, length approx. 2000 m.
wavelength approx. 17 km
Small antenna?

## Slide 6: Small antenna
Electrically small: the largest dimension of the antenna is at or under λ/2
Physically small: small compared with human size. Such as at or under the size of your hand

## Slide 7: Small antenna
We here mainly deal with antennas that are both electrically and physically small
  At or under λ/2 electrically
  At or under hand size physically
One of learning outcomes for the lecture!

## Slide 8: Stub/helical antennas
Flextronics Corporate Presentation
Bluetooth Stub Antenna GSM Stub Antenna
There are normally wires or metal strips inside the plastic cover

## Slide 9: Laminate Antenna
Flextronics Corporate Presentation
Flexible Laminate Antenna

## Slide 10: Dual Antenna Prototype for UMTS
Flextronics Corporate Presentation
Antenna
elements
PCB
Transmission line
SMA
connectors
Diversity antenna

## Slide 11: Lecture 8 Small Antennas – Part 1
What is a small antenna?
Monopole and dipole antennas
Loop antenna
Helical antennas
Slot antennas
Yagi antennas
Log-periodic wideband antennas

## Slide 12: Monopole and dipole
baluns
Monopoles
Dipoles

## Slide 13: Balun
Balun: an electronic device for connecting a balanced transmission line to an unbalanced one
Most baluns were designed experimentally
Balun is difficult to model analytically
Numerical modeling is used nowadays
Coax-fed dipole
must have balun

## Slide 14
consisting of two conductors of the same type, each has equal impedances along their lengths and to ground
  Twin lead
  Coupled microstrip line
  Coplanar waveguide
whose conductors have unequal impedance with respect to ground
  Coaxial cable
  Microstrip line
  Single-wire lines
Balanced transmission line
Unbalanced transmission line

## Slide 15: The most famous balun
The 300-to-75-ohm TV balun
Balanced
Unbalanced

## Slide 16: Ultra-wideband Balun
microstrip line
(unbalanced)
twin line
(balanced)
substrate

## Slide 17: Approximate current distribution of monopole on ground plane
The real current distribution:
  varies with length and radius
  compute it numerically for very accurate data
When the length L<λ/2 and the pole is thin:
  very good approximate current distribution analytically

## Slide 18: Approximate current distribution of monopole on ground plane
Thin wire approximation:
  current floats on the center line of the pole
Current distribution:
Correction for length l:
Accurate only when l<λ/2
Prime means source location

## Slide 19: Use imaging to solve the problem Now it is a problem of dipole!
Current after imaging:

## Slide 20: Quiz: What we have ingored in the modeling for monopole
The magnetic current in the opening!

## Slide 21: Approximate current distribution of dipole
The real current Distribution over dipole:
  varies with
    Thickness (radius) of the poles;
    Length of the poles;
    Size of feed gap;
    Surrounding structure,
      such as feed line,
      balun,
      shield around feed line,
      ground plane
  need to solve it numerically for accurate data

## Slide 22: Approximate current distribution of dipole
Good approximation analytically with assumptions:
  infinitesimal feed gap
    Very small feed gap
  thin wire approximation
    Current flows on the axis of poles
  use effective length
    To take into account of effect of the thickness of the poles
  neglect the effect of the transmission line and the balun

## Slide 23: Approx. current distr. of dipole
  infinitesimal feed gap
  thin wire approximation
  use effective length
  Neglect transmission line and balun

## Slide 24: Monopole on ground plane and dipole in free space
Have the same analytical formula for current distribution
Can be analyzed in the same way

## Slide 25: Which differences we should notice when we use the result of dipole in free space to get the result for Monopole on ground plane ?
The radiation function is valid only in up half space for monopole
  Directivity of monopole is 3 dB higher than that of dipole.
The input impedance of monopole is half of that of dipole.

## Slide 26: Current distribution of dipole with arbitrary orientation
excitation
current distribution
Orientation, unit vector
Dipole with arbitrary orientation

## Slide 27: Radiation field function of dipole
Radiation field:
Incremental dipole factor:
Fourier transform factor:
From vector integral far-field formulas (4.35):
Radiation function:
Radiation function consists of 3 parts:
Excitation:
ηI0

## Slide 28: Fourier transform
Analytic Fourier transform:
Fourier transform factor:

## Slide 29: Example: vertical halfwave dipole
,
then
Radiation field function:
BOR0 type antenna
z
x
y

## Slide 30: Y-polarized halfwave dipole
y-directed with
and
)
G
d
y
q
j
,
(
)
C
k
h
I
0
q
j
q
ˆ
sin
cos
j
j
ˆ
cos
+
(
)
j
˜
q
j
,
(
=
2
k
-
-
-
p
2
-
-
-
q
j
sin
sin
è
ø
æ
ö
cos
1
q
j
sin
sin
(
)
2
–
[
]
¤
=
j
˜
q
j
,
(
)
z
x
y
From the definition, not BOR antenna
…but almost BOR1…

## Slide 31: Normalized E-plane radiation pattern

## Slide 32: 3D radiation pattern

## Slide 33: Radiation Patterns
Since almost BOR1 antenna, we can use BOR1 formula to have
Because does not change much with φ

## Slide 34: BOR1 efficiency for y-dir. dipole

## Slide 35: BOR1 efficiency Definition

## Slide 36: Short dipole
Triangular current distribution gives the radiation integral
Radiation field function becomes the same as that of an
incremental dipole of half length, i.e.

## Slide 37: Directivity of short dipole
Power integral:
Directivity:
i.e. 1.76 dBi

## Slide 38: Radiation resistance of short dipole
Radiated power:
Radiation resistance:

## Slide 39: Example of radiation resistance of short dipole
In addition, short dipole has also a large reactance
Is it positive or negative, i.e. inductive or capacitive?
It is negative, i.e. capacitive.

## Slide 40: Directivity and radiation resistance of halfwave dipole in free space
At resonance frequency, the reactance is zero.

## Slide 41: Dipole impedance
G: Conductance
B: Susceptance
R: Resistance
X: Reactance

## Slide 42: Dipole fed by 50 ohm line

## Slide 43: Arbitrary dipole above PEC ground plane
PEC plane
For upper half space:
Under the ground plane:

## Slide 44: Vertical dipole above ground
For short dipole:
Ground plane factor

## Slide 45: Vertical dipole above ground

## Slide 46: Vertical dipole above ground: Directivity and radiation resistance

## Slide 47: Vertical monopole above ground
Total current distribution of the monopole plus its image is the same as for the dipole. Therefore,
The power integral becomes half that of the halfwave dipole
Therefore, the radiation resistance of the monopole is
Radiation function valid only for up half space!
3dB higher directivity
Monopole’s impedance is only half of that of dipole!

## Slide 48: Horizontal dipole above ground
error

## Slide 49: Horizontal short dipole & ground: Directivity and radiation resistance
Calculated from value of power integral

## Slide 50: Reflection coefficient for horizontal dipole above ground

## Slide 51: Lecture 8 Small Antennas – Part 1
What is a small antenna?
Monopole and dipole antennas
Loop antenna
Helical antennas
Slot antennas
Yagi antennas
Log-periodic wideband antennas

## Slide 52: Small loop antenna as a vertical magnetic dipole (BOR0)
Thin wire approximation
Constant current around ring ( a<<λ)

## Slide 53: Small loop antenna radiates as a vertical magnetic dipole (BOR0)
Radiation field function:

## Slide 54: Lecture 8 Small Antennas – Part 1
What is a small antenna?
Monopole and dipole antennas
Small Loop antenna
Helical antennas
Slot antennas
Yagi antennas
Log-periodic wideband antennas

## Slide 55: Helical antennas
Spiral shaped wire (thin wire approximation)
Best designed by using previously published experimental data and
wire modeling codes.

## Slide 56: Helical antennas: Two basic operation cases (Modes)
Very short helical antenna
vertical magnetic dipole
Polarization?
where L1 is the length of one turn.
Main beam direction?
And total length N×L1<<λ

## Slide 57: Helical antennas: Two basic operation cases (Modes)
B) Travelling wave mode (resonant loop):
Right wound
Radiation function

## Slide 58: Helical antennas: Two basic operation cases (Modes)
B)Travelling wave mode (resonant loop):
Right wound

## Slide 59: Helical antennas: Two basic operation cases (Modes)
B)Travelling wave mode (resonant loop):
along positive z-axis
Right wound
RHC polarization

## Slide 60: Co- and crosspolar radiation patterns of resonant loop

## Slide 61: Comparison
Short helical
  Main beam direction
    Omni azimuth
  Polarization
    Linear horizotal
Resonant loop helical
  Main beam direction
    z axis
  Polarization
    Circular
z
x
y
z
y
x
NOTE that our analysis is without ground plane.

## Slide 62: Lecture 8 Small Antennas – Part 1
What is a small antenna?
Monopole and dipole antennas
Loop antenna
Helical antennas
Slot antennas
Yagi antennas
Log-periodic wideband antennas

## Slide 63: Slot antennas
Undesired slots in shields:
  Electromagnetic compatibility (EMC) problems
  Antenna measurement chambers often shielded
Desired slots in antennas:
  Fed by waveguides
  Linear array
  Planar array antenna
  Cheap to manufacture
  Very accurate numerical models

## Slide 64: Slot: Field distribution
Slot resembles a short rectangular waveguide, with basic TE10 mode field. Therefore, the field distribution over a slot is:
  Good approximation even for thin wall
  Not effected much by type of excitation
  Not effected much by form and shape of ground plate

## Slide 65: Slot: Radiation function using equivalent magnetic sources
E
0
m
E
s
l
o
t
z
ˆ
´
E
0
p
x'
l
¤
(
)
x
ˆ
cos
=
=

## Slide 66: Slot: Radiation function
Incremental magnetic source factor:
Fourier transform factor:
Radiation function:
Excitation:
Radiation function consists of 3 parts:

## Slide 67: Slot: Radiation function
Directivity 3 dB larger than dipole

## Slide 68: Comparison
Dipole
z
x
y

## Slide 69: Lecture 8 Small Antennas – Part 1
What is a small antenna?
Monopole and dipole antennas
Loop antenna
Helical antennas
Slot antennas
Yagi antennas
Log-periodic wideband antennas

## Slide 70: Yagi-Uda antenna
A unidirectional (one direction only) antenna commonly used in communications for frequencies above 10 MHz
Commonly used as TV antenna

## Slide 71: Basic configuration of Yagi
Driven element
  a center-fed, half-wave dipole.
Reflector
  behind driven element.
  slightly longer than driven element.
Directors
  in front of driven element.
  shorter than driven element.
  typically one reflector and several directors.
Reflector
Driven element
Directors
Here F =300/λ

## Slide 72: Typical radiation pattern of Yagi For both E- and H-planes

## Slide 73: Characteristics of Yagi-Uda Antenna
End-fire antenna, not an aperture antenna
E-plane pattern and H-plane pattern are similar
  Even the E-plane and H-plane are very different in size
The gain does not increase linearly with the number of elements used.
  3-element Yagi has 5 to 6 dBi directivity.
  Adding another director results in a 2 dB increase.
  Additional directors have less and less effect.
  Adding more reflector has negligible effect.

## Slide 74: Yagi-Uda antenna
Now gain more attention at 60 GHz and above to THz.

## Slide 75: Lecture 8 Small Antennas – Part 1
What is a small antenna?
Monopole and dipole antennas
Loop antenna
Helical antennas
Slot antennas
Yagi antennas
Log-periodic wideband antennas

## Slide 76: Log-Periodic Dipole Array (LPDA)
Phase centre location varies with frequency

## Slide 77
Two parallel dipoles over ground (Eleven configuration)
  equal E- and H-plane patterns
  Beamwidth constant with frequency
  phase center is locked to the ground plane
  low far-out sidelobes and backlobes.
Decade bandwidth by
  Logperiodic
  Folded dipoles
Eleven Antenna – a decade bandwidth log-periodic antenna

## Slide 78
Several Projects on Eleven Antenna
For use in Green Bank
radio telescope for 150 – 1700 MHz
For use in RATAN telescope
for 500 – 3000 MHz
GMRT
for 200 – 800 MHz

## Slide 79
Measured Radiation Patterns in 45 deg plane of Eleven Antenna for 1 – 13 GHz

## Slide 80: Measured reflection coefficient of Eleven Antenna for 2 – 13 GHz

## Slide 81: Learning outcomes of the Lecture
Describe the definition of small antennas.
Describe at least five small antennas.
Describe characteristics of the radiation function of these small antennas, such as the directivity and radiation resistance.
Explain the analysis models for these small antennas.

## Slide 82: Next lecture
Small antennas part 2
  Microstrip patch antennas
  Inverted F-antennas
  Planar Inverted F-antennas
  Miniaturization